## Slide 1
Augsburg University of Applied Sciences | Faculty of Mechanical and Process Engineering
Brno University of Technology | Faculty of Mechanical Engineering |
Institute of Process and Environmental Engineering
Projektování a řízení procesů (KPJ)
Conceptual Design of Distillation, Absorption
and Stripping Systems
Prof. Dr.-Ing. Marcus Reppich
Room D5/249
 marcus.reppich@hs-augsburg.de
Important notice: These documents are to be used exclusively for study purposes, they are made available to participants of the lecture Conceptual Design of Distillation, Absorption and Stripping Systems (Projektování a řízení procesů, KPJ) at the Institute of Process and Environmental Engineering at the Brno University of Tech-nology only.
Cover image: Copyright by BASF SE

## Slide 2: Conceptual Design of Distillation, Absorption and Stripping Systems Timetable and Contents of Lectures and Exercises
Lectures |  |  | 
19.11.2013 | P 09 | Fundamentals of Binary Distillation | 
26.11.2013 | P 10 | Types of Distillation Columns | 
03.12.2013 | P 11 | Design of Distillation Columns | 
Exercises |  |  | 
19.11.2013 |  | Assignment date | 
26.11.2013 | C 10 | Design of a Multicomponent Distillation System Using the Process Simulation Software CHEMCAD (group work of two students, elaboration of a final project report) | 
03.12.2013 | C 11 |  | 
10.12.2013 | C 12 |  | 
13.12.2013 |  | Due date | 

## Slide 3: 2 Types of Distillation Columns Tray Column Design
Source: A. Mersmann, M. Kind, J. Stichlmair: Thermal
Separation Technology. Berlin, Heidelberg: Springer 2011
Symbols | 
a | downcomer
b | tray support
c | sieve trays
d | man way
e | outlet weir
f | inlet weir
g | side wall of downcomer
h | liquid seal
Aac | active area
Ad | downcomer area
Dc | column diameter
dcap, v, h | bubble cup, valve, hole diameter
H, z | tray spacing
hcl | height of down-comer clearance
hw | weir height
lw | weir length
lL | length of liquid flow path
 | relative free area
Characteristic dimensions
of industrial tray designs
wG

## Slide 4: 2 Types of Distillation Columns Design Principles of Packed Columns: Tower with Structured Packing (A); Tower with Structured-Packed Top Bed and Random-Packed Bottom Bed (B)
Symbols | 
a | liquid distributor
b | liquid collector
c | structured packing
d | support grid
e | man way
f | liquid re-distributor
(A)
(B)
Sources: A. Mersmann, M. Kind, J. Stichlmair: Thermal Separation Technology. Berlin, Heidelberg: Springer 2011; D.W. Green (ed.): Perry´s Chemical Engineers´ Handbook, New York: McGraw-Hill 2008

## Slide 5: 2 Types of Distillation Columns Examples of Distillation Column Internals
Source: GEA Wiegand GmbH, Ettlingen
Sieve Tray
Bubble Cap Tray
Tunnel Cap Tray
Struktured Packing

## Slide 6: 2 Types of Distillation Columns Examples of Distillation Column Internals
Floating valve tray with rectangular-shaped valves
(BDH™ valve)
Source: Sulzer Chemtech AG
Detail of Varioflex valve tray
Source: Koch-Glitsch, Inc.

## Slide 7: 2 Types of Distillation Columns Examples of Distillation Column Internals Common Random Packings
Common random packing particles
made of metal, plastic, ceramic
Sorce: Koch-Glitsch, Inc.

## Slide 8: 2 Types of Distillation Columns Examples of Distillation Column Internals Historical Development of Characteristic Random Packings
First Generation (Raschig Ring, Berl Saddle)
1895 to the 1950s
simple shapes with closed surfaces, robust
and stable design, cost-effective production
Second Generation (Pall Ring, Intalox Saddle)
late 1950s to the early 1970s
surfaces with cutted windows and bent tongues,
improved area distribution lowering pressure
drop and enhancing capacity
Third Generation (Net/Grid Structures, IMPT Ring)
late 1970s to the 1990s
framework structure, large free cross section,
low pressure drop, high efficiency
Fourth Generation (Raschig Super-Ring)
late 1990s until present
lower pressure drop and better mass transfer
efficiency

## Slide 9: 2 Types of Distillation Columns Examples of Distillation Column Internals Common Types of Structured Packings
Sources: Sulzer Chemtech AG; Koch-Glitsch, Inc.
Structured packing of corrugated metal sheets
Structured packings Mellapak
made of metal and plastic
Fitting structured packing elements Flexipac to a large-diameter tower

## Slide 10: 2 Types of Distillation Columns Comparsion of Tray and Packed Columns
Tray Columns |  | Packed Columns | 
 | cross flow of the two phases on the trays |  | countercurrent flow of the two phases
 | always used in columns of large diameters and towers that have more than 20 to 30 equilibrium stages, in applications with liquid rates of 30 m³/(m²h) and above, when liquid flowrate is high relative to vapor flowrate |  | packings are generally more expensive than plates, less expensive than tray columns for small column diameter (D<0.6 m), used in lower liquid-rate-applications (i.e. less than 50 m³/(m² h)
 | various tray types made of metallic materials (D=500–10000 mm) |  | more choices in materials of construction especially in corrosive service (e.g. plastic, ceramic, metal alloys, carbon), random (D=50–800 mm) or structured packings (D=20–11000 mm)
 | high liquid residence time |  | less liquid entrainment, low liquid holdup, especially suitable for thermally sensitive material
 | pressure drop is rather high, typically 7 mbar per equilibrium stage (not well suited for vacuum services) |  | lower pressure drop, typically 0,1 to 0,5 mbar per equilibrium stage (important in vacuum distillation)
 | dirty service (tray columns are easier to clean) |  | cleaning of a packing section is much too complica-ted and expensive
 | stable and robust operation of the separation process, more flexible to variations in operating conditions |  | foaming liquids can be handled more readily (less agitation of liquid by the vapour)
 |  |  | due to novel developments of packing elements the industrial use of packed columns is steadily increasing

## Slide 11: 2 Types of Distillation Columns Overall View of a Distillation Unit
Source: GVWU mbH, Norderstedt
Condenser
Cooling Water
Feed
Feed
Distillate
Distillate
Cooling Water
Steam
Bottom Product
Cooling Water
Bottom Product
Cooler
Feed Preheater
Distillate
Pump
Pump
Distillate
Cooler
Reboiler

## Slide 12: 2 Types of Distillation Columns Piping and Instrumentation Diagramm of a Distillation Unit
Source: Baerns, M. et al.: Technische Chemie. Weinheim: WILEY-VCH 2006